## Slide 1: ChoiceNet
Rudra Dutta, CSC, NCSU
SAS Lunch presentation, April, 2012
Internet Architecture Research
(What does THAT mean.)
(… and some other stuff)

## Slide 2: Future Internet – Concerns, Steps
In 2005-06, NSF created the FIND program
  ~ 20 projects funded in first round
  ~ 50 total in three years
What would the global network look like in 15 – 30 years, and how could it be built from scratch?
  How could left-by-wayside design goals be satisfied?
Underlying concern: incremental may not get us there
  Not new, but deeper
  Assumptions, priorities, “baked-in” in Internet – invisible walls
  Seeds of GENI – later
Compete and collaborate
http://www.nets-find.net/

## Slide 3: Internet Roots – and Sunlight
Continuity – over loss of networks/gateways
Support multiple comm. service types
Accommodate variety of networks
Permit distributed management
Cost effective
Low barrier to host entry
Resources must be accountable
Security; trust, availability
Support pervasive computing, mobile, wireless
Clark, 88, “Design Philosophy of the DARPA Internet Protocols

## Slide 4: FIND Priorities
Application-oriented architectural view
Security, trust; E2E  T2T
Economics
Social/regulatory
Flexibility, “Evolvability”
“Tussles”

## Slide 5
?
Are the same protocols right for every application?
Every host? Every physical medium?
Is flexibility good?
If everything is flexible, is there “a network” left?
What is “a network”, anyway?
If change is (or is supposed to be) a way of life in the Internet, is anything ever “wrong” with it?
Can you really “design for change?”
Is it true that a community is smarter than any individuals, in the long run?
Are the current network protocols the right protocols?
Are there any “right” protocols?

## Slide 6: A Reconstructed Protocol Stack
Transport
Network
Data Link
Physical
Physical Channels
App
App
App
Transport
Tuning
strategies,
hints
App
App
App
Physical Channels
m11
m31
m21
m42
m62
m11
m13
m21
m21
m31
m31
m43
m62
m61
Cross-
Service
Tuning
silo &
service
mgmt
Composability
Constraints

## Slide 7: Service Composition
Ontology of services
  Constraints on composition
    Relations - “requires”, “not / above” “not / immediately above”
  Application provides some service requirements
    “Need encryption”
Composition
  Find a permissible ordering for (expanded) set of services
Later - ontology as a repository for :
  Recipes, policies, tuning strategies, reasoning about performance effects

## Slide 8: Ontology - Networking Knowledge
Primitive
ServiceFunction
ServiceType
Constraint
Method
Service
Functional
Primitive
Compound
Simple
Ordering
Primitive
Functional
Encryption
ErrorCorrection
AddressLookup
Segmentation

## Slide 9: Software Architecture
App
class SILO_API {
public:
SILO_API() {
//silo_id = 0;
_request_id_init=0;
}
//build up a set of requires/forbids constraints
//such as: APP requires/forbids services A->B->C->NULL
ERROR_CODE create_required_srv (int request_id, list<srv_ID> srv_list);
ERROR_CODE create_forbidden_srv (int request_id, list<srv_ID> srv_list);
ERROR_CODE release_request(int request_id);
//...
};
// manages a collection of silos and passes data through them
class SiloManager {
public:
typedef unsigned int RecipeId;
typedef unsigned int SiloId;
static SiloManager &Instance();
// process data
void ProcessTxBuffer(const SiloId &siloId, unsigned char *buf);
void ProcessRxBuffer(const SiloId &siloId, unsigned char *buf);
// register a silo, load the needed DSOs
RecipeId RegisterRecipe(const string &recipe);
// remove a recipe
void DestroyRecipe(const RecipeId &recipeId);
// create a new silo given a recipe ID
SiloId CreateSilo(const RecipeId &recipeId);
// delete a silo
void DestroySilo(const SiloId &siloId);
RecipeId GetRecipeIdForSilo(const SiloId &siloId);
class SILO_Knob
{
public:
SILO_Knob() { ; }
inline int get_max() {return _knob_intf.nMax;}
inline int get_value() {return _knob_intf.nValue;}
inline bool set_value(int nValue) {
_knob_intf.nValue = nValue;
return true;
}
//...
};
Ontology of Services,
Composability Constraints,
Recipes, Tuning Strategies
Method
Method
Method
Method
Method
silo
SILO Management
SILO Tuning
SILO Construction

## Slide 10: Market-Enabling Architecture
John Musacchio, Jean Walrand, Venkat Ananthram, Galina Schwartz, Shyam Parekh
  User should be offered choice between network services and informed of benefits, then the market can play itself out
  Security could be achieved by “security insurance” provided by Certification Agency

## Slide 11: Service Choice
Users offered real-time choice: “red” and “blue”
  “Red” and “blue” not specified to users in detail
  ISP incentivized to improve along dimensions that matter
  Unlike ATM, IntServ, DiffServ, service definitions not standardized
John Musacchio

## Slide 12: Internet Today – Security Inadequacy
Users do not bear full cost of poor computer maintenance
Drivers do not bear full cost of reckless driving.
Liability insurance incentivizes drivers to be careful.
ANALOGY
John Musacchio
Zzzz

## Slide 13: Markets for Security
Example:
  Users pay to be certified by a Certification Agency (CA)
  CA takes on liability for attacks traced back to user
  CA incentivized to encourage users to take due care
$
Zzzz
John Musacchio
OS Update
Antivirus Update

## Slide 14: Postcards from the Edge
Roy Yates, Dipankar Raychaudhuri, Sanjoy Paul, James Kurose
Cache-and-forward
  Reliable hop-by-hop transport of large files
  Push-pull architecture for opportunistic delivery of files both to and from the wired network
  Enhanced naming to provide location information for mobile terminals
  Distributed caching of popular content to make peer-to-peer file sharing a first-class service and to enable efficient reliable multicast.

## Slide 15: Architectural Support for Selectively-Connected End Systems
Mark Allman, Vern Paxson, Ken Christensen, Bruce Nordman
Enable an energy-efficient future Internet
Baked-in assumption of always-on
  Fate sharing
  Soft-state
  E2E
Study how architecture should change for real current devices
  Proxy, “limbo”, assistant

## Slide 16: Future Internet Architecture
In 2009-10, NSF created the FIA program
  Build on FIND, NetSE, leverage GENI
  Integrate; nearly complete architectures
Four large projects funded
  Named Data Networking
  Mobility First
  Nebula
  eXpressive Internet Architecture
Similar focus as FIND, but also
  Economic viability
  “Deployabilty”, (“realizability”?)
http://www.nets-fia.net/

## Slide 17: ChoiceNet
NSF NeTS Large project
  Inducted into FIA
Team:
  University of Kentucky: Jim Griffioen, Ken Calvert
  North Carolina State University: Rudra Dutta, George Rouskas
  RENCI: Ilia Baldine
  University of Massachusetts: Tilman Wolf, Anna Nagurney

## Slide 18: ChoiceNet Principles
Expose choices throughout protocol stack
Interactions between technological alternatives and economic interactions
“Encourage alternatives”
  Provide building blocks for different types of services
“Know what happened”
  Ability of evaluate services
“Vote with your wallet”
  Reward good services through “money protocol”
Encourage
Alternatives
Know What
Happened
Vote with
Your Wallet

## Slide 19: ChoiceNet Architecture

## Slide 20: ChoiceNet Example
Choices for movie streaming
  Technical choices: different connections, transport, caching, etc.
  Economic choices: pay more for better experience
User experience
  Offer better service for a price
ChoiceNet infrastructure
  Identify choices, compose suitable offering
  Distribute money among providers
  Verify performance (or determine whom to blame)

## Slide 21: ChoiceNet Research
Research thrusts
  Technologies for alternatives
    Routes, transport, services, etc.
    Verification and payment
  Choice and composition
    Presentation of choice
    Measurement architecture
    Ontological approach
  Economics of choice
    Pricing, matching
    Incentives, cooperation vs. competition
Cross-thrust issues
  Predictability, stability
  Interface to user/apps
  “blocks”, “players”
  End-to-end scaling
Prototype
  GENI prototype
  Component prototyping
  Long-standing GENI experiment
  Addressing scalability
  Teaching use
  Assessment

## Slide 22: Questions Abound
Users – “chusers” ?
  Producers / consumers / intermediaries
  Which actors have influence over what
Economic Viability
  Industry structure and business models
  Provider ecosystem
Control / Policies
  Which actors have ability to block communication?
Interfaces among actors
  Information exchanged between providers?
  Inter-provider agreements?
  Negotiation and cooperation between providers?
Trust, Isolation, and Availability
  Instrumentation and data gathering
  Detection of non-functioning actors and response

## Slide 23: GENI
In late 2000’s, an NSF initiative to create a national-scale sharable network testbed
Allow researchers to experiment with a national “at-scale” footprint
Allow experimentation with different architectures, fundamentally incompatible
Virtualized underlying infrastructure indispensable for such a testbed
  Different experiments would be completely isolated
  Would use completely different stacks, hops
Also the thought: maybe virtualization is the next architecture

## Slide 24: Network Integration
Vision of integrated services network
  Single network infrastructure which carries traffic for various types of use
But – requirements are very different
  Integrating networks requires making “greatest of all networks” (ATM) rather than “least of all networks”
  Raises barrier to entry
Separate networks are good
  For banking and videochat and telesurgery, e.g.
But frustrating that “solved” problems reappear, old solutions cannot be easily applied

## Slide 25: Motivation for Virtualization
Approach similar to compute virtualization
A substrate that provides basic capabilities
A method to identify smallest units (“slivers”) of
  Bandwidth
  Switching
  Buffers
Resources that make up substrate must each be sliverable
  Easiest when slivering is along physical lines (NICs, switches)
Collection of slivers makes up a virtual network (“slice”)
  Similar to a virtual machine
Advantage of integrated network without (some of) the drawbacks

## Slide 26: GENI Conceptual Design Infrastructure to support at-scale experimentation
Mobile Wireless Network
Edge Site
Sensor Network
Federated International Infrastructure
Programmable & federated, with end-to-end virtualized “slices”
Heterogeneous,
and evolving over time via
spiral development
Deeply programmable
Virtualized
Notes: 26

## Slide 27: Moral of this story
GENI is meant to enable . . .
  Trials of new architectures, which may or may not be compatible with today’s Internet
  Long-running, realistic experiments with enough instrumentation to provide real insights and data
  ‘Opt in’ for real users into long-running experiments
  Large-scale growth for successful experiments, so good ideas can be shaken down at scale
A reminder . . .
  GENI itself is not an experiment !
  GENI is a suite of infrastructure on which experiments run
GENI creates a huge opportunity for ambitious research!
Notes: 27

## Slide 28: Resource discovery Aggregates publish resources, schedules, etc., via clearinghouses
What resources can I use?
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
These
GENI
Clearinghouse
Researcher
Notes: 28

## Slide 29: Slice creation Clearinghouse checks credentials & enforces policy Aggregates allocate resources & create topologies
GENI
Clearinghouse
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
Create my slice
Notes: 29

## Slide 30: Experimentation Researcher loads software, debugs, collects measurements
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
Experiment – Install my software,
debug, collect data, retry, etc.
GENI
Clearinghouse
Notes: 30

## Slide 31: Slice growth & revision Allows successful, long-running experiments to grow larger
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
Make my slice bigger !
GENI
Clearinghouse
Notes: 31

## Slide 32: Federation of Clearinghouses Growth path to international, semi-private, and commercial GENIs
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
Make my slice even bigger !
GENI
Clearinghouse
Components
Aggregate D
Non-NSF Resources
Federated
Clearinghouse
Notes: 32

## Slide 33: Operations & Management Always present in background for usual reasons Will need an ‘emergency shutdown’ mechanism
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
GENI
Clearinghouse
Federated
Clearinghouse
Components
Aggregate D
Non-NSF Resources
Oops
Stop the experiment
immediately !
Notes: 33

## Slide 34: Spiral 1 integration and trial operations Five competing control frameworks, wide variety of substrates
Components
Aggregate A
Computer Cluster
Components
Aggregate B
Backbone Net
Components
Aggregate C
Metro Wireless
Reference
Design
Components
Aggregate A1
Computer Cluster
Components
Aggregate A2
Optical Network
Components
Aggregate A3
Metro Wireless
Cluster A
Components
Aggregate B1
Optical Network
Components
Aggregate B2
Sensor Network
Cluster B
Components
Aggregate C1
Computer Cluster
Components
Aggregate C2
Programmable Switches
Cluster C
Components
Aggregate D1
Optical Network
Components
Aggregate D2
Sensor Network
Cluster D
Components
Aggregate E1
Computer Cluster
Components
Aggregate E2
Optical Network
Components
Aggregate E3
Sensor Network
Cluster E
Components
Aggregate E4
Programmable Switches
Notes: 34

## Slide 35: GENI System Decomposition (simplified) Engineering analysis drives Spiral 1 integration
Operations
NSF Clearinghouse
Federations
Researchers
GENI Aggregates
Notes: 35

## Slide 36: OpenFlow
Open standard that attempts
  Virtualization
  Flow routing
Main idea: separate switching (forwarding) functionality from control logic/policy
  Use any box with forwarding mechanism to execute custom networking logic
  Basic isolation: OF traffic and regular traffic
  For OF, provide custom logic as flow definitions
  Also may attempt to detect flows
http://www.openflow.org/

## Slide 37: OpenFlow
OpenFlow is an API – off a Stanford project
Control how packets are forwarded
Implemented on hardware switch
PC
Hardware Layer
Software Layer
Flow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
TCP
sport
TCP
dport
Action
OpenFlow Firmware
*
*
5.6.7.8
*
*
*
port 1
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
PKT
Controller
OpenFlow Switch
IP dst: 5.6.7.8
OF
Protocol
PKT
1st packet
routing
following packets
routing

## Slide 38: Local Connection
Triangle
  Duke U (Jeff Chase, CS) and RENCI (Baldine, Huang) are architects of GENI-ORCA
    One of four control frameworks
  RENCI coordinated BEN is part of GENI substrate
  Good working partnership resources
NCSU
  Lead in one GENI project (Integrated Measurements Framework), PI: Dutta; subcontractors: RENCI, Columbia U
  Three years, $480K (till Oct 2012)
  Build messaging plane for measurement and actuation events, enable cross-layer
  Two more 3-Year projects (as subcontractor) in Oct 2011
    GENI rack – equipment only: “standard” rack of equipment with compute, comm, s/w
    GENI GIMI – larger integration of I&M, main involvement in years 2 and 3

## Slide 39: GENI Futures
Follows fairly strict and professional software release practices
(Very large) wiki to keep all informed of all corners of GENI
Research
  May become litmus test for seriousness of research proposals, results
  Expanding into computing and storage resources
Connections with other initiatives

## Slide 40
XML-RPC
XML-RPC
pS client

## Slide 41: GMS Demo
Generating client certificates/credentials
Cert/cred generate
(gcf)
Openfire web portal
Openfire logs
Client credent
-ials
Chat clients
+ certs
Repo service
+ certs
Repo DB
IMF PSM logs
OMF-like EC + RC
+ certs
OMF-like AM
Flukes
Chat client communication
OMF-like EC-RC experiment
Replace OMF EC cert  connect fails
Restore cert, expire credentials  connects, msg fails
Start Repository service  show RC / PSM msgs archived
OMF EC-like (stub)
GENI Messaging Service (XMPP)
OMF RC-like (stub)
GENI CA
CA Cert
GENI Cert
GENI Cert
GENI Cert
Chat
GENI Cert
Repository Service
Client credentials

## Slide 42: Campus GENI Infrastructure
“GENI campus”
  At a minimum: houses a rack providing VMs, switching, OF and understanding GENI Control Framework, fronting some experimental resources to GENI experimenters
  Full scale: All or a large part of campus network is GENI-fied, OF-aware
  Federation benefits
Currently trying for NSF CC-NIE program
  Supplementary or transformational high-bw infrastructure
  Not GENI-specific but strong encouragement

## Slide 43: CentMesh – Original Vision
Prove and transition IT research in pervasive computing and cybersecurity
Part of original SOSI proposal - also funded by DURIP grant – both from ARO
In planning and design/development (and permissions!) for 2+ years
Equipment ordering now mostly complete
In process of deployment – ITng (OSCAR Labs) overseeing
The Centennial Mesh project aims to build a highly programmable, extensible, open, outdoor wireless testbed to support research and education on the design of wireless mesh networks, as well as IT systems and applications enabled by wireless mesh networks, using open source code built by NCSU students and faculty, and re-using other open source code

## Slide 44
Zones 1, 2, 3
Commercial Testbed Node
Experimental Testbed Node
Commercial
Testbed
Experimental .
Testbed
In-bldg ncsu/guest, outdoor coverage
Physical Proximity,
Power Control
Operational
Slicing/sharing at wire access,
Throttling (duty cycle)
experimental at MAC,
(Channel Control)

## Slide 46: CentMesh Nodes

## Slide 47: Software Architecture
Central control/management node
All control/signaling traffic is channeled through the communicator module
  Embeds control plane policies such as spectrum usage
  Uses TCP connections between mgmt and mesh nodes
  Uses automatic pub/sub mechanism locally, manual/programmatic pub/sub across nodes (planned extension to complete automatic pub/sub in future)

## Slide 48: Software Architecture
Mgmt node contains a data repository
  Acts as decoupling intermediary between various data collection/dissemination procedures
Management software modules implemented in general as paired managers and agents
  Managers and agents are clients to communicator
  Managers interact with data repository

## Slide 49: Software Architecture
Servers for typical OAM tasks also attaches to data repository
  Clients may run on control node or elsewhere on Internet
  Visualization currently implemented this way
  Scripting planned to work this way (will adapt from past existing testbed implementation)

## Slide 50: Using CentMesh Software (or not)
BIOS
Multi-stage boot
System
Core
User
“Images”

## Slide 52: CentMesh Research
CentMesh : Smart programmable Wireless
Augmented Reality Apps
Network Design
Social Sciences
Transportation Planning
Smart Grid

## Slide 53: Redundant Routing (Diffuse/Disjoint)

## Slide 54: Improving Wireless Back-pressure
A
C
B
E
D
F
6
2
9
3
Urgency weight
(1) on CD for E = 9K - 6K = 3K
(2) on CD for F = 3K - 2K = 1K
How to allow medium access that is urgency-proportional in presence of varying packet size traffic?

## Slide 55: Impact of Power Control in Mesh
`
`

## Slide 56: Autonomous Smart Sensor

## Slide 57
Sensed Data
Sensed Data,
Digested Data
Location Control
Data request,
priority

## Slide 58
Information sharing with neighbors
Local Directives
Individual Sensor Mission
Sensing & Movement
Information Diffusion
Platoon Mission
Regional Directives
Global Digests
Global Directives
Platoon Organization
Stability
Swarm control
Decompose model
Hierarchical
messaging
Model sparse data
Joint optimi-zation
Predictive control

## Slide 59
Battery
CentMesh Node
(existing)
WiFi cards
Battery charger
Sensing, Command
Orchestration
ABORT
FM Transmitter
FM Receiver
Motor
Propellor
Airframe
BBBK WiFi
BBBK
Sensors on
breadboard
Autopilot/
controller

## Slide 60
centmesh.csc.ncsu.edu
itng.ncsu.edu

## Slide 61: 3) Decoupling Measurement and Analysis
Marker Mechanism:
Measuring and matching the same “metric” across MPs
User’s sending rate may vary
Add “marker” information to application PDU
Timestamp the first marker packet M1 as t1
Count the number of bytes, called B till the next marker packet M2 received at t2
When M2 is received, send( 2, t1, t2, B ) as MD
Granularity is based on the user

## Slide 62: 3a) Simple Throughput Measurement
One-way delay measurement across MPs
Time (s)
Chart: 
Marker Sequence Number
Delay (ms)
Time (s)

## Slide 63: 3a) Simple Throughput Measurement
Overhead benefit comparison;
Based on the results of previous research papers
Using rough calculations and approximations
At least one order of magnitude less network load than all existing approaches
This is of the nature of “easy way to do difficult problem”
Chart: KB
| pathchar | clink | pchar | nettimer | pathchirp | spruce | pathload | marker
overhead | 2075 | 1120 | 2205 | 380 | 300 | 300 | 6250 | 20
Accuracy: >50%
Accuracy: 10%-20%

## Slide 64: 3b) Jitter Apportionment for Video Streaming Experience Quantification
Chart: Time (s)
At this level of data examination, NSP3 is clearly to blame

## Slide 65: 3b) Jitter Apportionment for Video Streaming Experience Quantification
Chart: Time (s)
Freeze | 0 | 0 | 0 | 0
Glitches denote the losses and Freezes denote video player freezes
A freeze
A glitch

## Slide 66
Analysis for freeze 1 [t=6 and t=10]
 | Mean % | Std dev % | Max J %
NSP1 | 96.7 % | 93.8 % | 94.7 %
NSP2 | 0.2 % | 0.6 % | 0.2 %
NSP3 | 3.1 % | 5.6 % | 5.1 %
 | Mean % | Std dev % | Max J %
NSP1 | 98.5 % | 97.2 % | 97.2 %
NSP2 | 0.0 % | 0.0 % | 0.0 %
NSP3 | 1.5 % | 2.8 % | 2.8 %
Analysis for freeze 2 [t=8 and t=12]
Chart: Time (s)
| 6.332 | 6.53 | 6.734 | 6.936 | 7.14 | 7.33 | 7.73 | 7.932 | 8.134 | 8.332 | 8.532 | 8.724 | 8.928 | 9.128 | 9.326 | 9.532 | 9.76 | 9.968 | 10.166
mp1 owd | 145.37 | 69.27 | 48.6 | 51.05 | 143.51 | 151.06 | 116.77 | 89.57 | 114.98 | 119.43 | 123.24 | 147.78 | 141.41 | 96.06 | 163.39 | 146.37 | 139.46 | 135.5 | 163.2
mp2 owd | 176.88 | 101.28 | 80.11 | 82.56 | 175.01 | 182.57 | 148.28 | 121.07 | 146.49 | 150.93 | 154.74 | 179.29 | 172.92 | 127.57 | 194.89 | 177.87 | 170.97 | 167 | 194.7
Chooser owd | 185.19 | 114.02 | 87.88 | 90.33 | 182.78 | 190.34 | 158.58 | 128.85 | 154.26 | 158.91 | 162.51 | 187.06 | 181.13 | 135.34 | 202.66 | 185.64 | 178.74 | 174.7 | 202.4
Glitch | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Freeze | 0 | 0
Jitter at Chooser | 71.17 | 26.14 | 2.45 | 92.45 | 7.56 | 158.58 | 29.73 | 25.41 | 4.65 | 3.6 | 24.55 | 5.93 | 45.79 | 67.32 | 17.02 | 6.9 | 4.04 | 27.7
Delay (ms)
Freeze 1 is at t=8s
Freeze 2 is
at t=10s
  3b) Jitter Apportionment for Video Streaming Experience Quantification
Systematic analysis produces “apparent surprise”: NSP1 is equally to blame

## Slide 67: Working Application of Optical Equipment Control in GENI
XML-RPC
XML-RPC
 Make it possible for measurements to be exchanged between substrates and GENI slices
 XMPP server enhanced with GENI credentials for authentication/authorization
 Different modes for real-time measurement/actuation loop suitable for control, and offline archival
 Plugs in with perfSONAR and OMF if desired, also carries NetKarma event records
 Early demonstration at GEC8, GEC12, GEC13
 Video stream between hosts, through Polatis / Infinera
 BER / port power measurements from optical layer to stack protocol
 Attenuate one path, application switches to another path
 Improves video
 Rudimentary but shows promise of approach
Integrated
Measurement
Framework

## Slide 68: What is CentMesh ?
CentMesh : a project to build a versatile, open source shared resource on campus
Provide an active testbed to support research and instruction on wireless networks
Part of NCSU’s “Living Laboratory” vision
An extensible, programmable, open, real outdoor wireless network
A teaching and research resource at NCSU Centennial
centmesh.csc.ncsu.edu

## Slide 69: Who Built CentMesh ?
Homemade !
  Built by NCSU student researchers
  Guided by NCSU faculty
  Funded by Army Research Office and NCSU
  Operationalized by Institute of Technology of Next Generation (ITng), NCSU

## Slide 70: Designing CentMesh
Modular programming library
Clear separation of data, control, management functions
Easy to innovate in some or many parts, keep others unchanged
Currently working on sensor/actuator expansion
  SmartAir (see Sichitiu talk)
Ideally suited for instrumenting of networking and distributed computing, human mobility, transportation, …
A general-purpose testbed for analytic tool/science ?

## Slide 71: Control Theory
Collaboration with U New Mexico, funded by Science of Security Lablet
  Many computing/networking things can be seen as feedback systems
  Use control theory to characterize
Characterize routing policies by reachability analysis of linear system description
  Multihop wireless (redundant routing algorithm), OLSR

## Slide 72
Example
7
8
9
6
5
4
3
1
2
Nodes: {1,2,…,9} Links: {e12,e14,e23,…,e89} = 12 total
Goal is to reach node s = 9
Possible controls:
Link state q: if all links are working at time 0
i.e. once we choose a feasible node to move to given qt, we move to that node with probability 1
State transition function:
with
So at each time step we choose a node ut to travel to based on current location and current state of the links.
Our “look-up table” is given by the function , which tells us where to go next based on current state. We find by solving
Link costs:
i.e. c12=1, c14=2, etc.
1
2
1
1
3
2
4
2
2
3
4
3
We also include “holding” cost of 5 if we choose to stay in same node, i.e. cii=5

## Slide 73
Solution: Dynamic Program
Time N (Working backwards):
  Set
Time k = N-1, …, 1:
  For i = 1,…,8 (don’t include node 9 because once at node 9, we stay there with 0 cost)
    For ( )
      Define as the set of nodes packet can reach from node i given link conditions described by state q. If is empty, set u=i and incur cost cii.
      Set
At time k=1, gives shortest expected path (expected value of shortest path) starting from node i with starting link conditions q.
We also have the function which provides a look-up table indicating which node to travel to at time k+1 given packet is in node i at time k, and link conditions are described by q.
with M a large number

## Slide 74
Results
Expected shortest path length (cost) starting from each node, given all links are active at time 1, i.e.
Over N=10 time steps (so packet must reach node 9 within 10 time steps), what are expected shortest path lengths given various starting link conditions?
Node | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 9.66 | 8.01 | 7.54 | 6.01 | 4.54 | 3 | 4.67 | 2 | 0
Node | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 12.05 | 8.06 | 7.58 | 6.06 | 4.58 | 3 | 4.70 | 2 | 0
Expected shortest path length (cost) starting from each node, given links (1,4) (2,3) are inactive at time 1, i.e.
Node | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | 13.79 | 9.74 | 8.35 | 7.74 | 5.35 | 3 | 14.8 | 10.74 | 0
Expected shortest path length (cost) starting from each node, given links (8,9) (7,8) are inactive at time 1, i.e.

## Slide 75
Time | K=1 | K=2 | K=3 | K=4
Node |  |  |  | 
1 | 4 | 2 | 2 | 2
2 | 5 | 5 | 1 | 1
3 | 6 | 6 | 6 | 2
4 | 5 | 5 | 5 | 5
5 | 6 | 6 | 6 | 4
6 | 9 | 9 | 9 | 9
7 | 8 | 8 | 8 | 8
8 | 9 | 9 | 9 | 9
9 | 0 | 0 | 0 | 0
Look-up Table when all links are up at each step (same as deterministic shortest path algorithm). Here N=5, so that packet must reach Node 9 within 5 time steps, in order to demonstrate what happens to routing algorithm when a packet cannot reach destination in time.
Routing Policies
Note: Because we are limited to 5 time steps, after time k=2, Node 1 can no longer make it to Node 9 in time, Node 2 cannot make it to Node 9 after k=3, etc. This is why we see consistent routing for each node up to the time when it can no longer make it, at which point it tries to minimize link traversal costs without having a destination. Hence we see that the packet bounces back and forth between Nodes 1 and 2 when it does not have time to reach Node 9. Without a time constraint, we would get a time-independent routing table identical to column 1.
1
3
2
9
8
7
4
5
6

## Slide 76
Time | K=1 | K=2 | K=3 | K=4
Node |  |  |  | 
1 | 2 | 2 | 2 | 2
2 | 5 | 3 | 5 | 5
3 | 6 | 6 | 6 | 6
4 | 5 | 5 | 5 | 5
5 | 6 | 6 | 6 | 6
6 | 9 | 9 | 9 | 9
7 | 8 | 8 | 8 | 8
8 | 9 | 9 | 5 | 5
9 | 0 | 0 | 0 | 0
Look-up Table when links (1,4) and (2,3) are down at times k=1 and k=2, then at time k=3 those links become active and link (8,9) goes down. Algorithm is run for N=10 time steps, but only show policies for time k=1 to k=4.
Routing Policies
1
3
2
9
8
7
4
5
6
Blue arrows indicate policy at times k=1 and k=2. At time k=3, links conditions change and policy switches to red arrows. Because of the longer time horizon, we get the consistent, stationary policy at earlier times.

## Slide 77
Reachability Under Various Controllers
Chart: 
Centralized Controller | 0.9665 | 0.9857 | 0.9936 | 0.9857 | 0.9936 | 1 | 0.9936 | 1
Fixed Controller | 0.2031 | 0.4967 | 0.8322 | 0.4967 | 0.8322 | 1 | 0.8322 | 1
Semi-Fixed Controller | 0.1671 | 0.4125 | 0.6658 | 0.4125 | 0.6658 | 1 | 0.6658 | 1
Node
Prob. Of Reaching Node 9 in N time steps
N=10, All links up at time 0
Chart: 
Centralized Controller | 0.8072 | 0.9004 | 0.9682 | 0.9004 | 0.9682 | 1 | 0.9682 | 1
Fixed Controller | 0.008 | 0.104 | 0.488 | 0.104 | 0.488 | 1 | 0.488 | 1
Semi-Fixed Controller | 0.0208 | 0.1476 | 0.4214 | 0.1476 | 0.4214 | 1 | 0.4214 | 1
N=5, All links up at time 0
Node
Prob. Of Reaching Node 9 in N time steps
Centralized controller has complete knowledge of link states at all times
Fixed controller uses shortest path routing table at each time step (as calculated on slide 5). If prescribed link is down, packet is held at current node
Semi-Fixed controller only knows link states adjacent to current node. Assumes all other links are up, and picks forwarding node from shortest path routing if available, otherwise picks next best option using pre-computed controller (as in slide 3) and believed link states.
*I changed the probability of a link going down to 0.1 from 0.05 in this case.
In this example, while perfect knowledge is obviously best, it seems consistently better (i.e. higher probability of reaching node 9) to hold a packet until the optimal link becomes available rather than to send it to another node without knowing the full state of the network.

## Slide 78: Shortest Path Length Under Various Controllers
Controllers same as previous slides. Let the algorithm run for 20 time steps to calculate expected shortest path length. Length greater than 20 indicates the likelihood that packet will not reach node 9 within 20 time steps.
Node
Expected shortest path length
Shortest path calculated using same dynamic program as before, only setting all edge costs to 1, including holding cost. Problem is that initial shortest path is set to a large number for all nodes but 9 in order to “drive” packet to node 9. Need to find another way to calculate shortest path length to not get the large numbers seen above when there’s a large probability packet does not reach node 9 in 20 time steps.
Chart: 
Centralized Controller | 5.063 | 3.6015 | 2.3878 | 3.6015 | 2.3878 | 1 | 2.3878 | 1
Fixed Controller | 68.3262 | 30.2304 | 9.5128 | 30.2304 | 9.5128 | 1 | 9.5128 | 1
Semi-Fixed Controller | 125.9178 | 82.9616 | 44.9815 | 82.9616 | 44.9815 | 1 | 44.9815 | 1